Legal Notice

Town of Whately

INVITATION FOR BIDS

FOR THE

MANUFACTURE AND INSTALLATION OF MODULAR

STORAGE VAULT IN TOWN OFFICES

TOWN OF WHATELY

4 SANDY LANE

WHATELY, MA 01373

The Town of Whately Select Board invites sealed bids for the manufacture and installation of a Modular Storage Vault in the Town Offices.  The project includes the manufacture and installation of a Modular Storage Vault in the Town Offices under the direction of the Town Administrator.    Bids for this project are subject to the provisions of MGL Chapter 30, Section 39M and to the payment of prevailing wages.

Bids shall be submitted to:  Town Administrator, Town of Whately, 4 Sandy Lane, So. Deerfield, MA  01373.  Deadline for bid submittal is 11:00 a.m. on Thursday, March 23, 2017.  Bid packages can be obtained at the above address, Monday -  Thursday from 8  a.m. to 4 p.m. and Friday from 9 a.m. - Noon, by e-mailing townadmin@whately.org, or on the town’s website www.whately.org or by calling (413) 665-4400.  Anyone obtaining bids on the website should also inform the town of such so if any addenda are issued they will be notified.

Paul Newlin, Chair

Board of Selectmen

Post:			Whately Town Offices, www.whately.org

Publish:		Daily Hampshire Gazette

Central Register

Town of Whately

INVITATION FOR BIDS

FOR

MANUFACTURE AND INSTALLATION OF MODULAR

STORAGE VAULT IN TOWN OFFICES

TOWN OF WHATELY

The Town of Whately Select Board invites bids for the manufacture and installation of a Modular Storage Vault in the Whately Town Offices located at 4 Sandy Lane, Whately.  Specifications can be obtained from the Select Board’s Office, Town of Whately, 4 Sandy Lane, South Deerfield, MA  01373  Monday - Thursday between the hours of 8:00 a.m. and 4:00 p.m. and Friday from 9 a.m. - Noon or by e-mailing townadmin@whately.org., or downloading from www.whately.org. Anyone obtaining bids on the website should also inform the town of such so if any addenda are issued they will be notified.     Estimated cost for this work is not to exceed $109,000.

Deadline for bid submittal is Thursday, March 23, 2017 at 11:00 a.m.  Bids must be delivered or mailed to: Town Administrator, Town of Whately, 4 Sandy Lane, South Deerfield, MA  01373.

Scope of Work

The scope of this project is to manufacture and install a 18’ x 20’ by 9’10” outside dimension modular vault in the Whately Town Offices.  Sub bids for electrical, HVAC and Drywall will be handled separately by the Town of Whately.

Please Note: Prevailing Wages apply to this project. Prevailing wage schedule can be viewed on our website at www.whately.org or can be requested by mail by calling 413-665-4400.

DESCRIPTION OF WORK

A. The Work of this Section includes all labor, materials, tools, and equipment needed to furnish and install modular fire vault as specified below.

B. The Work includes, but is not limited to:

1. Modular fire vault.

2. Vault doors.

3. Steel structure for vault.

4. Accessories.

C.  Intent:  A major intent of the work of this section is to provide a structurally independent,  complete records storage vault which meets the requirements of the Commonwealth of Massachusetts and specified performance criteria.

RELATED WORK to be performed by others under separate contract.

A. Carefully examine all the Contract Documents for requirements which affect the Work of this Section.

B. The following work will be performed by others under separate contract.

1.  Light Fixtures and electrical work for the vault:

a. All dust & vapor resistant light fixtures within the vault, all conduit and electrical service for light fixtures.  An emergency back-up, trickle –charge light fixture as required for egress from the vault in a power failure.

b.  Electrical requirements for fire alarms, fire suppression system, smoke detectors and convenience outlets.

2. Drywall finish inside the vault for walls & ceiling – Galvanized Steel Firring strips and 5/8” fire rated drywall on the interior vault walls and ceiling as well as the exposed exterior vault walls.  Tape, float and paint finish per owner’s requirements.

3.  Water Sprinkler Systems – Piping and heads as required by owner.

4. HVAC System requirement to service the vault interior and provide environmental control over the interior of the vault.

The Town of Whately will pull all required permits for the project including building and welding permits as required.

The Town of Whately will supply 208/230 volt circuit with a 30 Amp breaker to provide necessary power for welding on site.

REGULATORY REQUIREMENTS: Comply with applicable provisions of the following reference codes and standards.   Recommendations made in the reference standards shall be considered mandatory requirements.

- Commonwealth of Massachusetts Performance Standards for Safes and Vaults.

- NFPA 232 – Protection of Records Standards

QUALITY ASSURANCE

- Source:

Provide pre-engineered, modular vault assemblies from one manufacturer.

Provide secondary materials and products which are acceptable to the manufacturer of

the primary vault package.

- Installer:

Installer shall have minimum of 5 years experience installing modular vaults and

be approved and authorized by the manufacturer of the vault.

- Design Loads:

Steel supports shall conform to structural loading requirements of the

Massachusetts Building Code and Commonwealth of Massachusetts Performance

Standards for Safes and Vaults, but in no case less than the following:

1. Live Load  : 350 lbs./sq. ft.

2. Impact Loads : Ample accommodation shall be made for protection against impact

loading by falling equipment or building members and against accumulations of

burning debris.

- Welding:

All welding shall be in compliance with the American Welding Society Code.

SUBMITTALS

- Product Data:

Submit manufacturer's product data, including installation instructions and recommended uses, for each material specified. Provide manufacturer's certifications stating that products and systems comply with requirements.

- Shop Drawings:

Provide large scale shop drawings for fabrication, installation, and erection of all parts of the Work. Provide plans, elevations, and details of anchorages, connections, and accessory items. Provide installation templates and instructions for work installed by others.

1. Structural Shop Drawings:

Provide complete design calculations for structural assemblies prepared by a structural engineer registered in the Commonwealth of Massachusetts. Structural shop drawings shall bear the registration stamp of the designing structural engineer.

DELIVERY, STORAGE, AND HANDLING:

Deliver, store, and handle in strict compliance with manufacturer's instructions and recommendations. Sequence deliveries to avoid delays and minimize on-site storage. Protect from all possible damage.

PART 2: PRODUCTS

MODULAR VAULT PANEL: Provide panel designed to meet applicable requirement of NFPA

232 Class 125-2 hr. protection of electromagnetic media and Class 350-6 hr. vault. Panels

shall have the following characteristics:

- Construction:

Panels shall consist of a high temperature (2000 degrees F melting point)

refractory fiber core enclosed on three longitudinal sides by expanded metal mesh with

structural steel supports at each corner. Vapor barrier of 20 gauge cold rolled sheet steel

shall be used to enclose fourth side of panel to seal the interior of the vault against

migration of steam into the vault enclosure. Edges of panels shall be tongue and groove

design with gasket seals for connection to adjacent panels. Gaskets shall be high

temperature fibrous insulation which meets Fire Resistance Classification ASTM E119

and UL263 Time/Temperature Curve. Panels shall be designed for horizontal or vertical

use.

- Size and Configuration:

Provide 2’ wide panels to meet the 18’ x 10’ by 9’10” exterior dimensions of the vault.

C. Fire Resistance:

When tested in accordance with ASTM E119 and UL 263 Time/Temp. Curve, panels shall achieve a rating of Class 125 Data Rating after 4 hour test. Maximum average temperature of unexposed face shall be no more than 125 degrees F.

D.  Acceptable Product:

Firelock CL-350/CL-125 or equal.

VAULT DOOR: Provide door assembly designed to meet applicable standards for Class 350-

6/Class 125-4 hr. insulation from heat migration through the vault enclosure.

A. Door assembly shall consist of a dual door entryway system with a clear opening of 36" wide X 78" high.

1. Exterior door shall be an insulated vault door with an UL 350-6 hour rating.

2. Interior door shall be installed utilizing a custom stanchion. Interior insulating door

shall be UL rated to 3 hour and 250 degrees F Rate of Rise Classification. Interior

door shall be gasketed to provide a vapor seal to prevent the migration of water vapor

into the vault or gas fire suppressant agents out of the vault.

3. Stanchions: Exterior doors shall be fastened to stanchion integral to modular wall

panels. Stanchion shall have high temperature (2300 degrees F) gasket strips at the

junction of the wall panel and stanchion. Interior door stanchion shall be fastened to

concrete floor with anchor bolts. Seal junction between interior and exterior door stanchions with insulating gasket strips.

B. Fire Resistance:

When tested in accordance with ASTM E-119 and UL 155 Time/Temperature Curve, door assembly in the closed position after a duration of 4 hour test shall not exceed 125 degrees F at the inner vault.

C.Closers:

Door system shall be equipped with electromagnetic closer-holder or equivalent.

The hold open position shall be capable of being set between 90 degrees and 180

degrees. Closers shall be electrically powered, employing a solenoid operated bullet

plunger valve. When energized, bullet plunger valve seals closer’s hydraulic closing

circuit. Unit must close door during any electrical power interruption, activation of integral

smoke detection and/or activation of  exterior smoke/heat alarm sensors.

1. Acceptable Product: LCN 4314 ME Series.

D.Emergency Escape:

Doors shall be equipped with inside escape mechanism to ensure life safety evacuation in the event that personnel are within vault during activation of door closure system.

CABLE TRAY: Provide cable tray assembly designed to meet applicable standards for Class

125-4 hour insulation from heat migration through vault enclosure. Cable tray assembly box shall attach to the vault exterior and include one 4" square electrical junction box mounted

both on the exterior face and interior face of vault panel. 1" diameter PVC conduit shall

penetrate vault panel to carry wiring to the interior of the vault. A UL rated firestop device

shall be used to seal cable tray conduit in the event of fire. Firestop device shall be attached

to a 20 gauge steel sheet at the interior face of the panel at the point of penetration. Fill

junction boxes with intumescent caulk.

FIRE DUCT SYSTEM: Provide fire duct system to allow environmental control of vault interior

by the building’s HVAC system. Fire duct system shall be designed to meet applicable

standards for Class 125-2 hour insulation from heat migration into vault enclosure. Provide

damper assembly consisting of three fire rated dampers located in series within a 16 gauge

galvanized steel housing. Each damper shall be held in the open position by use of 165

degree F fusible links. The duct shall be insulated with ceramic fiber and protected from

physical damage by an external steel jacket.

SUPPORTING STEEL STRUCTURE

- Steel Shapes:

ASTM A36.

- Steel Tubes:

ASTM A500 or A513.

- Grout:

Provide pre-mixed, non-staining, non-corrosive, non-shrink, non-metallic grout

complying with CE CRD-C588, type D, 5,000 psi. Acceptable products are:

1. "POR-ROK" expanding grout manufactured by Hallemite Manufacturing Co.,

Cleveland, OH.

2. "Embeco Pre-Mixed Grout" manufactured by Master Builders, Cleveland, OH.

3. An approved equal.

D. Accessory items include, but are not limited to fasteners, sleeves, and brackets. All

accessory items exposed to view shall match primary steel material in color and finish.

ACCESSORIES: Accessories shall include, but are not limited to:

A. High temperature fibrous insulation in moldable form which meets Fire Resistance

Classification ASTM E119 and UL 263 Time Temperature Curve.

ACCEPTABLE MANUFACTURER: Provide complete vault system manufactured by Firelock or equal.

EXECUTION

GENERAL

A. Execute all Work in accordance with manufacturer's recommendations and instructions except where the Specifications call for more restrictive requirements.

B. Inspection:

Inspect and verify all existing conditions and previous Work before beginning

this Work. Beginning Work means that the Installer accepts substrates, previous work,

and existing conditions.

COORDINATION:

Coordinate with Town as to the Other Work to be performed to avoid project delays, to ensure dimensional accuracy, and to properly prepare for interior finishes and electrical and HVAC connections.

- Electrical:

Coordinate location and requirements of lighting and power to vault.

- HVAC:

Coordinate location and size of HVAC duct serving vault.

- Finishes:

Coordinate with the Town the timing of proper installation of interior wall, floor, and ceiling finishes.

INSTALLATION:

Install Work plumb, true, and square. Anchor floor track securely to existing concrete slab. Seal joints between panels and existing structure with high temperature moldable fibrous insulation. Cover all internal panel structural members with fiber strips.

ADJUSTING AND REPAIR

- Adjusting:

Adjust vault doors to work easily, smoothly, and correctly.

- Repair:

Repair minor damages so that there is no evidence of repair. Remove and replace Work which cannot be satisfactorily repaired.

General Information and Bid Submission Requirements:

# General:  Bids will be accepted during business hours (Monday - Thursday between the hours of 8:00 a.m. and 4:00 p.m. and Friday from 9 a.m. - Noon) until the deadline of Thursday, March 23, 2017 at 11 a.m.  at which time they will be opened and read aloud.  The official submittal time shall be measured according to the Eastern Time Zone provided by the National Institute of Standards and Technology.  Bids must be delivered or mailed to arrive by the deadline to: Town Administrator, Town of Whately, 4 Sandy Lane, South Deerfield, MA 01373.  Bids must be submitted in a sealed envelope marked “Modular Vault Bid”.  This bid is governed by the provisions of MGL Chapter 149.

All bids must include a non-collusion form, tax compliance certificate, a certificate of corporate vote (in the case of corporations), and at least three recent references.  All bids must be signed by an authorized individual(s).

All bidders must supply a bid bond of 5% of the value of the total bid.

The successful bidder will be required to supply a 50% payment bond based on the value of the total bid.

The contract will be awarded within sixty (60) days after the bid opening.  The time for award may be extended for up to 75 additional days by mutual agreement between the Town and the apparent lowest responsive and responsible bidder.

If any changes are to be made to this Invitation for Bids (IFB), an addendum will be issued.  Addenda will be mailed, e-mailed or faxed to all bidders on record as having picked up the IFB.

Questions concerning this IFB must be submitted in writing to:  Brian Domina, Town Administrator, 4 Sandy Lane, South Deerfield, MA  01373 before 4 p.m. on Thursday, March 9, 2017.  Questions may be delivered, mailed, e-mailed to townadmin@whately.org  or faxed (413-665-9560).  Written responses will be mailed, e-mailed or faxed to all bidders on record as having picked up the IFB.

A bidder may correct, modify, or withdraw a bid by written notice received by the Town prior to the time and date set for bid opening.  Bid modifications must be submitted in a sealed envelop clearly labeled “Modification No. ___”. Each modification must be numbered in sequence, and must reference the original IFB.

There will be an optional site visit and pre-bid conference on March 2, 2017 at 10:00 a.m. at the Whately Town Offices, 4 Sandy Lane, Whately, MA.

The bidder by making a bid represents that the bidder has read and understands the bidding documents, and that the bid is made in accordance therewith.  By submitting a bid, the bidder further represents that he or she has complied with the intent to visit the site, become familiar with local conditions under which the work is to be performed and has correlated the bidder’s personal observations with the requirements of the contract documents.  In addition, the bidder represents through his or her bid that the contract documents are sufficient in scope and detail to indicate and convey understanding of all terms and conditions for performance of the work of this contract.

The bidder shall carefully study and compare the bidding documents, shall examine the site and local conditions, and shall at once report to the Board of Selectmen errors, inconsistencies or ambiguities discovered.

The Town of Whately retains the right to cancel this IFB, or to reject in whole or in part any and all bids, if the Town determines that cancellation or rejection serves the best interests of the Town.

The Town of Whately reserves the right to waive informalities, and to reject any bid if the Town determines that such bid does not represent the bid of a person or agency competent to perform the work.

All bid prices submitted in response to this IFB must remain firm for one hundred twenty (120) days following the bid opening.

Authorized Parties:  A bid must be signed as follows: 1) if the bidder is an individual, by her/him personally; 2) if the bidder is a partnership, by the name of the partnership, followed by the signature of each general partner; and 3) if the bidder is a corporation, by the authorized officer, whose signature must be attested to by the clerk/secretary of the corporation and the corporate seal affixed.

Bid Evaluation:  All bids shall be evaluated by the Municipal Building Committee, Selectmen, Town Clerk and the Town Administrator.

Plans and Specifications:  Technical specifications are made an integral part of these IFB documents.

Pricing:  All bidders must provide an inclusive price for all services and materials described on the attached Form for Bidders

QUALIFICATIONS OF BIDDERS – Please provide documentation that you meet these qualifications.

Bidders must perform all the requirements contained in this Invitation for Bids, including all attachments, amendments (if any), and appendices.

Bidders must have a minimum of five (5) years satisfactory performance on similar projects.  Bids are subject to review of references and a positive determination from the bid evaluators of all available references.  The Town reserves the right to reject any bid which, in its judgment, fails to meet the requirement of this IFB or which is incomplete, conditional, or obscure; or which contains additions or irregularities; or in which errors occur; or if determined to be in the best interest of the Town to do so.  The Town reserves the right to waive minor discrepancies or permit a proposer to clarify such discrepancies and so conduct discussions with all qualified proposers in any manner necessary to serve the best interests of the Town.

The company receiving the award shall provide a certificate of liability insurance of not less than $1 million per occurrence and naming the Town of Whately as additional insured, and must also carry Workman’s Compensation Insurance as required by law.

The contract will be awarded to the responsive and responsible bidder offering the lowest price for the contract as per the provisions of MGL Chapter 149 using MGL Chap. 30 Section 39M.

Whately Town Offices Modular Vault Bid

Bids Due 11 a.m. on Thursday, March 23, 2017

Name of Bidder: _______________________________________________

Address: _____________________________________________________

Telephone #: ____________________	Fax #: _____________________

E-mail: ____________________________________________________

BASE BID

Labor			$ ___________________

Materials		$ ___________________

Other Costs		$ ____________________

TOTAL BASE BID				$ _____________________

Submitted By:  _________________________________________________

(Signature of Person Authorized to Bind Bidder)

Name (please print): _____________________________________________

Additional Signatory if Necessary:___________________________________

Name (please print):______________________________________________

## CERTIFICATE OF NON-COLLUSION

The undersigned certifies under the penalties of perjury that this bid or bids has been made and submitted in good faith and without collusion or fraud with any other person.

As used in this certification, the word “person” shall mean any natural person, business, partnership, corporation, union, committee, club, or other organization, entity, or group of individuals.

_____________________________________________________

(Signature of person signing bid)

_____________________________________________________

(Name of Business)

CERTIFICATION AS TO PAYMENT OF STATE TAXES

Pursuant to M.G.L.v.62C, S49A, I certify under the penalties of perjury that the Contractor has complied with all laws of the Commonwealth of Massachusetts relating to taxes.

_____________________________				_____________________________

Social Security Number or						Signature of Individual or

Federal Identification Number					Corporate Name

By: _____________________________

Corporate Officer

(If applicable)

CERTIFICATE OF VOTE

(Corporations Only)

At a duly authorized meeting of the Board of Directors of the

_________________________________________ held on ____________________

(Name of Corporation)             				(Date)

it was VOTED that

_________________________		_________________________

(Name)					(Officer)

of this company, be and hereby is authorized to execute contracts and bonds in the name and on behalf of said company, and affix its corporate seal hereto; and

such execution of any contract or obligation in this company’s name on its behalf by such officer under seal of the company, shall be valid and binding upon this company.

I hereby certify that I am the clerk of the above named corporation and that _________________________ is the duly elected officer as above of said company, and that the above vote has not been amended or rescinded and remains in full force and effect as the date of this contract.

________________________		_________________________

Date						(Clerk)

Corporate

Seal

REFERENCES

Reference 1:

Name and Address of Reference: ___________________________________________

______________________________________________________________

Telephone Number of Reference: _________________________________________

Name of Project Owner: ________________________________________________

Address of Project: ____________________________________________________

Brief Description of Work: ______________________________________________

Reference 2:

Name and Address of Reference: ___________________________________________

______________________________________________________________

Telephone Number of Reference: _________________________________________

Name of Project Owner: ________________________________________________

Address of Project: ____________________________________________________

Brief Description of Work: ______________________________________________

Reference 3:

Name and Address of Reference: ___________________________________________

______________________________________________________________

Telephone Number of Reference: _________________________________________

Name of Project Owner: ________________________________________________

Address of Project: ____________________________________________________

Brief Description of Work: ______________________________________________